38	linux下的汇编

Grammar summary
pushl %eax	-- use % as prefix
pushl $1	-- use $ as immediate operands
addl $1,%eax -- source and target are reversed comparing with Intel ASM
movb val,%al --- the word length of an operation is based on the last character, b w l -->byte 8, word 16, long 32 . In Intel,that is “mov al,byte ptr val”
Abosulte jmp and call should add “*” as prefix,which is not needed in Intel
ljmp $section,$offset --- jmp far section:offset , jmp as ljmp
icall $section,$offset --- call far section:offset , call as icall
lret $stack_adjust ---- ret far stack_adjust
IMPORTANT
in AT&T ASM, address looking up is “ section:disp(base,index,scale) ”, which is “ [section:base+index+scale]” in Intel.
The actual offset is disp+base+index*scale
Examples:	movl -4(%ebp),%eax
movl array(,%eax,4)
movw array(%ebx,%eax,4)
movb $4,%fs:(%eax)

Hello World and System Call
#hello.s – ends with s
/*C note*/
.data
msg: .string “Hello,world!\\n”
len = . - msg
.text
.global _start #the label starts with _

_start:
movl $len,%edx #arg 3 , c call , in stack , the last argument enters firstly
movl $msg,%ecx #arg 2
movl $1,%ebx #fd = 1 , stdout
movl $4,%eax #sys_call = 4 -->sys_write
int $0x80 #0x80 means system call,similar to libc

movl $0,%ebx
movl $1,%eax #sys_exit
int $0x80
$as -o hello.o hello.s #generates object file
$ld -s -o hello hello.o #link objects , -s means ommit symbols
You can look at include/asm-i386/unistd.h to find all system call

Intel
;hello.asm
section .data
msg db “Hello,world!\\n”
len equ $ - msg
section .text
.global _start

_start:
movl edx,len
movl ecx,msg
movl ebx,1
movl eax,4
int 0x80

movl ebx,0
movl eax,1
int 0x80
$nasm -f elf hello.asm #intel asm tool

- Other gramar
  1. every statement is ended with ; or newline . The last statement should always end with newline
  2. like as C, you can use \newline to ommit newline interpretation
  3.format of statement is
  label : .asm_command annotation # note that command starts with .
  label :movl op1,op2 annotation #instruction does not start with .
4.string , number are the same with c \n=newline \b=back
5.single char use ‘A.means ‘C=67
6. zero-extention and sign-extention are movz[bwl][bwl] and movs[bwl][bwl]
7.instruction prefix code
  for example , --------- repne scas %es:(%edi),%al , scan string repeatly.The prefix repne does the loop until some condition
8. a * indicates that the jmp/call has no thing to do with PC , otherwise it is always related to PC.
Sections
Whether explicitly mentioned or not , there are always 3 sections in output of asm file:
text , data,bss
where text is at address 0 ,afterwards are data and bss in order.
There is also a section named .absolute .It is used for ld to link object files.In linking multiple object files , ld has to resize all the sections in each file .But the absolute section changes nothing.
Generally, ld will place all .data (.text and .bss) together to get a huge big .data section.
Sub sections
if you want several data separated in different files to be allocated together , you can use grammar like .text 0 , then all data in .text 0 will be gathered together.if no sub section assigned , .text 0 is used.(.data 0 the same)

- Symbols
  label is current value of asm counter
use “=” to assign a symbol value
“.org xxx” is the same with “. = xxx” ; you’d to know that “.” is a constant symbol that denotes the current counter value.
A symbol has several properties : name , value ,type. For every symbol in seciton text,data,bss,absolute , the value of a symbol is the address ( may not be offset ) of that position.And except absolute,the value will change if ld has changed the base address of the section.That’s why absolute called absolute.It’ll never change the symbols inside it.Looking up include/a.out.h to see the information about symbol.
ASM command(case insensetive)
1.	.align x	----	the border align command
2.	.ascii “string” – no null char appended
3.	.asciz “string”
4.	.byte arrays	---- .byte 1,3,8 (a byte for every expression)
5.	.comm symbol,length ---- declare a public named area in bss
6.	.data [n]
7.	.desc symbol,abs-expr
8.	.fill repeat,size(up to 8,default 1),value(4 bytes long) ------ if size >= 8, then it is resized to 8. produce repeat*size bytes with value
9.	.global/.glob symbol	---- get the symbol from current file,not from others.For ld.
10.	.lcomm symbol,length	---- allocate a local area (not seen by ld because of local) in bss
11.	.int/.long expression	---- like .byte , but length is 4-byte
12.	.octa expressions	---- octa 16-byte,.quad 8-byte,.word/.short 2-byte
13.	.org new_lc,fill	---- set current counter to new_lc
14.	.string “string”	---- same with .asciz,but treat \ as special character.
15.	.code16/.code32	–--change mode to 16/32

command line of as
-a list all programs
-f fast operation
-o
-R	combine .data and .text
-W	no warnings
command line of gcc
-S	generate asm file
-c	compile without link
-std=gnu99|c99|c89

embeded asm in C
__asm__(
“codes”\
:<list of output registers>\
:<list of input registers>\
:<registers that will be modified>);
__asm__ maybe used as ams.
Use %% to generate %.This is because gcc will treat % as special character to translate those codes into asm codes.
“=a” (value) ---- movl %eax,$value

- {...} and ({…})
  { } is used to combine several statement into one.Such statement usually is called compound statement.Note,there is no “;” after “}”.
  ({..}) is used as an expression in C,the value of which is lastt expression in { }.
  Generally, ({..}) is used to define macros.
  Res = 3 + ({x + 4;})+ 5 // { … ;} should always end with a “;”
  #define CMOS_READ(addr) ({\
  outb_p(0x80|addr,0x70);\
     inb_p(0x71);\
})
other declarations in C function
1.inline
2.volatile	----- a function will never return .Say if in a function , a system_exit is called
3.static	------ local function or variable
4.extern
5.

function call realization
ebp+4 ---- > return address ( for IP)
ebp ---- > last ebp
ebp – 4 --- > saved registers ,plus local variables
esp ---→ current stack top
eax as return value

the stack top is decreasing down.
Call
Ret

Some Advance
Carefully use as86 and as, because
as86 : mov ax,cs|ds is valid
but in as it is not.

Determining on which segment register used
Firstly , you can transfer data directly from memory to memory, there is just one memory address used in one instruction
movl 0(%esp),%eax ---- use ss
movl %eax,(%esp) ---- use ss
movl (%eax),%esp ---- use ds

the segment register is selected depend on the base register used.
As for esp,ebp ---→ss is default
As for eax,ebx,ebp --→ any other thing , ds is default

The usage of each Registers
eax
accumlation , the temporary results by division,adding,subtraction and minus
ebx
base address registers
ecx
in loop or string processing as a counter
edx
I/O port
Combine with eax to form bigger number
esp
with ss , pointing to the top of the stack
ebp
default is the current stack base
if used with prefix like cs:(or others) , it could be used to point other segment
esi
with ds: ,as the source address of the operands.With automactic increment of decrement
as changeable address in address-looking-up.e.g. (%ebx,%esi,4)
edi
with ds: ,as destination of operands.Similar to esi
cs , ds
ss
ss:(%ebp|%esp) is the only format that will be accepted.
Ss:(%eax|%ebx) will cause SIGV_ERROR.
es
an extended segment , for additional data.
Some innovation
you can’t set a value in one place of memory directly to another.
CS,EIP can’t be used as destination
in mov DST,SRC ; the optional modes are :reg-→reg,sreg-→reg,reg-→sreg.no others options.

In Real Mode
Real Mode is under 16-bit programming.Therefore, a segment register will store the index to a segment decripto no more, it directly stores the real address of the segment address.Thus , to compile a
real mode program, we should set the DS for ourselves.Generally routine is to use predefined constant @data like this:
mov ax,@data
mov ds,ax ; this is using masm. Linux does not support real mode.

Indirectly Addressing will only use SI,DI,BX . Sometimes may use BP.But BP is designed for stack generally.
In Protection Mode
eax,ebx,ecx,edx,esi,edi,ebp,esp
all can be used to indirectly addressing.(e.g not immediate numbers)
such an instruction will simplely assume the segment register:
movl 8(%ebp),esi ----- in C call , this means get the first argument. (The first one to fetch is the last one been push)
64 bit and 32 bit
in 32 bit , a word means a 4-byte trunck of memory. Thus , consider the instructions below:
pushw 0x3333 #esp=0x9e
movl 4(%esp),%eax #get eax=0x0
pushl 0x11112222 #esp = 0x96
mov 2(%esp),%eax #get eax=0x1111
popl %eax #normal
popw %ax #normal
So why is this result?
Image a stack pointer is
ESP-->	0xa0 [ ] --→when pushw , first move,then set value
0x9f [ 0x33]
0x9e	[ 0x33]
0x9d	[ ]
0x9c	[ ]
0x9b	[ ]
0x9a	[ ]
0x99	[ 0x11]
0x98	[ 0x11]
0x97	[ 0x22]
0x96	[ 0x22]	--→border
a word that is ABCD , stored in memroy is D C B A (from low to high).
Since ESP is down decreasing , ESP always points to the first BYTE of ABCD.(which is D)

when pushw 0x3333,
Generated Codes
After ld has generated the executable file, there is no symbol any more in the file.All symbols are actually constants hence were all replaced by an actually integer.The integer is an offset from the base of the whole program segment,not any single segment.
A code maybe like this:
movl $msg,%eax
mov $10,$ss:(%eax)
will be generated into:
movl	$0x60012f,%eax
movl $0xa,%ss:(%rax)
and because ds will be automactically applied to any that without a prefix, ds must be 0.

 the diagram above can verifies that conduction.

An important theme of coding ASM is to know what actual code the ld will generate for us.

Call ret jmp / lcall ljmp
Lcall
lcall $seg,$offset
RET
popw %ip
LJMP
ljmp new_segment,offset or ljmp *mem ( 48 bit length required)
equal to:
set the current segment to new,the set PC to offset.
Example 1:
ljmp $0x8, $protcseg
use 0x8 as the GDT selector,plus the offset protcseg.Result is goto gdt[0x8]+$protcseg.
Example 2:
ljmp *0x80
In memory 0x80,the higher 16-bit saves the seg_selector,the lower 32-bit saves the offset.Same as ljmp x[48-33],x[32-1]

boot up of system
1.The BIOS select a media to load booting up code
2.Load the first section(512Byte) of the media to the address of 0x7c00 ( 13 KB ),then JMP 0x7c00
3.The code starts to boot up the system.

A Linux typical boot loader and the header
driver:	[ boot.s ][ head.s ]
After the steps described above , boot.s starts to function.At this time, boot.s firstly uses BIOS Interruption 0x13 to load head.s into address of 0x10000(64KB),and afterwards transfers it into 0(the start of the memory).Then it sets CR0 to turn to Protection Mode,and jmp 0.
Why does not boot.s directly load head.s into 0?Because the BIOS IDT was then at there , which will be used to do that.Alternatively , we can directly jmp 0x10000 to start up head.s.
A Linux typical head/kernel initialization
The first head.s just do one thing: It has 2 subprocesses called A and B,and at every 10 ms, the main process switch the current task from one to another,from printing A to printing B.
1.reset the GDT
2.set the timer of the CPU clock
3.reset IDT
4.starting A.
Gernerally , the system is somehow and anyway a software , it also requires a context.But what makes it particular is that it uses GDT as its context , it will always find it’s segment information from the GDT.For each subprocess of the system, it generates a corresponding LDT for each of them.
- asdf
- asdf